|  | ......................... pcs. .............................. € .............................. € GEZE IQ box KNX For connection of the GEZE window drives IQ windowdrives to the KNX building system for intelligent natural ventilation. The IQ box KNX is compatible with the following GEZE window drives from software version 3.0: Spindle drive E 250 NT (also in RWA opening and locking systems) Chain drive Slimchain Chain drive Powerchain Locking drive Power lock Activation of the connected drives (position in %, speed in %) as well as feedback of the current position and window status (closed / open / opening / closing / position) is implemented by the KNX building bus. Ventilation functions gap ventilation and timed ventilation must be guaranteed without further controls. Technical data: Supply voltage 24 V DC,+-25 %, SELV Max. current drives 6 A Induced current intake to KNX bus 5 mA Induced current intake to 24 V 25 mA IP rating / protection rating IP 20 protection rating III Ambient temperature 5 °C…+70 °C Connection cross-section 24 V & drive 1.5 mm² Connection cross-section push button 0.5 mm² Max. overall length of drive cable 15 m Dimensions of flush-mounted housing (UP) 50 mm x 45 mm x 19 mm Dimensions of housing fitted to top hat rail (HS) 98 mm x 62 mm x 18 mm |
| --- | --- |
|  | ......................... pcs. .............................. € .............................. € ( ) Version flush-mounted housing ( ) Version housing fitted to top hat rail |
|  | ......................... pcs. .............................. € .............................. € Note: You also require a 24 V power supply to supply the window drives as well as the IQ box KNX. |
|  | ......................... pcs. .............................. € .............................. € ( ) Flush-mounted power supply ( ) Power supply fitted to top hat rail |
|  | ......................... pcs. .............................. € .............................. € Installation and functional test Installation and functional test by an expert authorised by the manufacturer. Function test using the open/close push keys of the IQ box KNX. |
|  | ......................... pcs. .............................. € .............................. € Start-up and official approval Official approval of the complete smoke and heat extraction system by an officially recognised expert, who also hands over the acceptance certificates. |
|  | ......................... pcs. .............................. € .............................. € Service maintenance - compact package Maintenance and testing of hold-open systems (optional position) Service package for maintenance and testing according to ASR A1.7 as well as according to manufacturer’s specification with the following performance features: - One maintenance per contract year - Free provision and updating of the test documents - Attachment of the inspection sticker - Fault diagnosis and repair jobs during the contract period will be carried out at reduced hourly rates - Service technicians will be deployed within 24 hours of the message being received from Monday – Friday between 7 am and 5 pm without surcharges - Personal availability at the help desk 24 hours a day, 365 days a year - Contract run time: 2 years |
|  | ......................... pcs. .............................. € .............................. € Service maintenance - comfort package Service maintenance (optional position) Comfort service package for maintenance and accident prevention inspection in accordance with ASR A1.7 as well as according to manufacturer’s specification with the following performance features: - Extension of the warranty to 36 months (condition: the maintenance contract is concluded 3 months after the commissioning date at the latest) - One maintenance per contract year - Free provision and updating of the test documents - Attachment of the inspection sticker - No separate charging for services and travel costs during the warranty period - No separate charging for consumables up to € 25 per maintenance - No separate charging for working hours when spare parts are replaced during the maintenance - Personal availability at the help desk 24 hours a day, 365 days a year - Contract run time: 3 years |
|  | ......................... pcs. .............................. € .............................. € Delivery and installation Wiring to be carried out on site by an electrical contractor according to the GEZE cable plan. Delivery, installation and commissioning through plant fitters or service partner. Safety analysis, instruction of the operator as to how the system works and handing over of the documentation. Annual maintenance and technical inspection by an expert authorised by the manufacturer incl. documentation of the inspection in an inspection log. |